## Slide 1
A GPU Based DSP Front End
605.417 Introduction to GPU Programming
Michael DiBerardino
Notes: Hello and welcome to my project presentation for Information Retrieval. My name is Michael DiBerardino.

## Slide 2
Introduction
Digital Signal Processing front end
  Gather RF from antenna
  Typically FPGA
  Real time streaming required
  High bandwidth
Information content low
  Compared to RF bandwidth
    100 MHz+
  Signal is heavily decimated
    Voice: 100 MHz to 44.1 KHz

## Slide 3
Idea
GPU’s combine parallelism with software
  Massively parallel
  Follow traditional software paradigms
  Faster to program than FPGA’s
    My current FPGA design at work takes 2.5 hours to compile
      One mistake equates to 2.5 hours of lost time!
Implement DSP front end in GPU
  Tune, Filter, Decimate

## Slide 4
The Math
Tune
  Complex multiplication
  Generate Sin & Cos
Filter
  1D convolution
    1 multiply per thread
  Parallel summation
    log2(n)
Decimate
  Modulo block id
  Restrict copies from shared to global memory

## Slide 5
The Code - CPU
Only 2 lines in Octave
  Involves library calls for decimation
Implemented in 1 thread

## Slide 6
The Code - GPU
Kernel is only a few lines long
Convolution is 6 lines
Down-sample is 3 lines

## Slide 7
Side by Side
CPU
  Octave
    Interpreted
  Double precision
  1 thread
GPU
  Cuda
    Compiled
  Single precision
  4096 blocks
    One block per sample
  64 threads
    1 thread per filter tap
    Sum 64 threads to get 1 data sample

## Slide 8
Side by Side
Chart: Execution Time vs Data Length
| 32 | 64 | 128 | 256 | 512 | 1024 | 2048 | 4096 | 8192 | 16384 | 32768 | 65535
GPU | 0.0844 | 0.0725 | 0.0897 | 0.0824 | 0.083 | 0.112 | 0.132 | 0.191 | 0.315 | 0.554 | 1.079 | 2.074
CPU | 5.782 | 4.522 | 4.535 | 4.586 | 4.579 | 4.759 | 5.034 | 5.673 | 6.627 | 8.821 | 13.321 | 22.34

## Slide 9
Side by Side
CPU result spectrum
  3 signals of interest
GPU result spectrum
  3 signals of interest

## Slide 10
Conclusion
Successful implementation
  GPU is
    Faster than CPU
      Roughly 10x
    Just as accurate as CPU
    Just as easy to code as CPU
    Easier to code than FPGA
CPU & GPU spectra look identical
  Minor variations in noise floor
    Possibly different LSB rounding schemes

## Slide 11
Future Work
Change decimation rate on the fly
  Recalculate filter coefficients
    Kaiser Window => Bessel functions
Include FFT
  Another function frequently handled by FPGA
  Can be made parallel
Max length is 65,535
  Incorporate cohearant, sequential runs
  Time interleave beginning and ending samples